## Slide 1: HW3 – Tomasulo with Speculation Template

## Slide 2: Cycle 1
Instructions | ROB Entry # | IS | EX | WB | CMT
LD F0, 0(R1) | 1 | 1 |  |  | 
DIVD F2, F0, F6 | 2 |  |  |  | 
LD F6, 8(R1) | 3 |  |  |  | 
DIVD F6, F6, F2 | 4 |  |  |  | 
SD F6, 16(R1) | 5 |  |  |  | 
DADDI R1, R1, #-32 | 6 |  |  |  | 
BNEQZ R1, LOOP | 7 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 1
Time (until complete) | Name | Busy | Op | Vj | Vk | Qj | Qk
 | Add1 |  |  |  |  |  | 
 | Add2 |  |  |  |  |  | 
 | Mult1 |  |  |  |  |  | 
 | Mult2 |  |  |  |  |  | 
 | Mult3 |  |  |  |  |  | 
 | Mult4 |  |  |  |  |  | 
Reservation Stations
Register Result Status
Reg | F0 | F2 | F6 | R1
ROB # | #1 |  |  | 
CDB | ROB #
LD/SD Buffers
Time (until complete) | Name | Busy | Addr | Qj
2 | Ld1 | Yes | 0+R1 | 
 | Ld2 |  |  | 
 | Sd1 |  |  | 
 | Sd2 |  |  | 
ROB Entry # | IS | EX | WB | CMT
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
12 |  |  |  | 
13 |  |  |  | 
14 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 2

## Slide 3: Cycle 2
Instructions | ROB Entry # | IS | EX | WB | CMT
LD F0, 0(R1) | Head 1 | 1 | 2- |  | 
DIVD F2, F0, F6 | Tail 2 | 2 |  |  | 
LD F6, 8(R1) | 3 |  |  |  | 
DIVD F6, F6, F2 | 4 |  |  |  | 
SD F6, 16(R1) | 5 |  |  |  | 
DADDI R1, R1, #-32 | 6 |  |  |  | 
BNEQZ R1, LOOP | 7 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 1
Time (until complete) | Name | Busy | Op | Vj | Vk | Qj | Qk
 | Add1 |  |  |  |  |  | 
 | Add2 |  |  |  |  |  | 
 | Mult1 | Yes | DIVD |  | F6 | #1 | 
 | Mult2 |  |  |  |  |  | 
 | Mult3 |  |  |  |  |  | 
 | Mult4 |  |  |  |  |  | 
Reservation Stations
Register Result Status
Reg | F0 | F2 | F6 | R1
ROB # | #1 | #2 |  | 
CDB | ROB #
LD/SD Buffers
Time (until complete) | Name | Busy | Addr | Qj
1 | Ld1 | Yes | 0+R1 | 
 | Ld2 |  |  | 
 | Sd1 |  |  | 
 | Sd2 |  |  | 
ROB Entry # | IS | EX | WB | CMT
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
12 |  |  |  | 
13 |  |  |  | 
14 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 2

## Slide 4: Cycle 3
Instructions | ROB Entry # | IS | EX | WB | CMT
LD F0, 0(R1) | Head 1 | 1 | 2-3 |  | 
DIVD F2, F0, F6 | 2 | 2 |  |  | 
LD F6, 8(R1) | Tail 3 | 3 |  |  | 
DIVD F6, F6, F2 | 4 |  |  |  | 
SD F6, 16(R1) | 5 |  |  |  | 
DADDI R1, R1, #-32 | 6 |  |  |  | 
BNEQZ R1, LOOP | 7 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 1
Time (until complete) | Name | Busy | Op | Vj | Vk | Qj | Qk
 | Add1 |  |  |  |  |  | 
 | Add2 |  |  |  |  |  | 
 | Mult1 | Yes | DIVD |  | F6 | #1 | 
 | Mult2 |  |  |  |  |  | 
 | Mult3 |  |  |  |  |  | 
 | Mult4 |  |  |  |  |  | 
Reservation Stations
Register Result Status
Reg | F0 | F2 | F6 | R1
ROB # | #1 | #2 | #3 | 
CDB | ROB #
LD/SD Buffers
Time (until complete) | Name | Busy | Addr | Qj
0 | Ld1 | Yes | 0+R1 | 
2 | Ld2 | Yes | 8+R1 | 
 | Sd1 |  |  | 
 | Sd2 |  |  | 
ROB Entry # | IS | EX | WB | CMT
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
12 |  |  |  | 
13 |  |  |  | 
14 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 2

## Slide 5: Cycle 4
Instructions | ROB Entry # | IS | EX | WB | CMT
LD F0, 0(R1) | Head 1 | 1 | 2-3 | 4 | 
DIVD F2, F0, F6 | 2 | 2 |  |  | 
LD F6, 8(R1) | 3 | 3 | 4- |  | 
DIVD F6, F6, F2 | Tail 4 | 4 |  |  | 
SD F6, 16(R1) | 5 |  |  |  | 
DADDI R1, R1, #-32 | 6 |  |  |  | 
BNEQZ R1, LOOP | 7 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 1
Time (until complete) | Name | Busy | Op | Vj | Vk | Qj | Qk
 | Add1 |  |  |  |  |  | 
 | Add2 |  |  |  |  |  | 
15 | Mult1 | Yes | DIVD | 0+R1 | F6 |  | 
 | Mult2 | Yes | DIVD |  |  | #3 | #2
 | Mult3 |  |  |  |  |  | 
 | Mult4 |  |  |  |  |  | 
Reservation Stations
Register Result Status
Reg | F0 | F2 | F6 | R1
ROB # | #1 | #2 | #4 | 
CDB | ROB #
 | #1
LD/SD Buffers
Time (until complete) | Name | Busy | Addr | Qj
 | Ld1 |  |  | 
1 | Ld2 | Yes | 8+R1 | 
 | Sd1 |  |  | 
 | Sd2 |  |  | 
ROB Entry # | IS | EX | WB | CMT
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
12 |  |  |  | 
13 |  |  |  | 
14 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 2

## Slide 6: Cycle 5
Instructions | ROB Entry # | IS | EX | WB | CMT
LD F0, 0(R1) | 1 | 1 | 2-3 | 4 | 5
DIVD F2, F0, F6 | Head 2 | 2 | 5- |  | 
LD F6, 8(R1) | 3 | 3 | 4-5 |  | 
DIVD F6, F6, F2 | 4 | 4 |  |  | 
SD F6, 16(R1) | Tail 5 | 5 |  |  | 
DADDI R1, R1, #-32 | 6 |  |  |  | 
BNEQZ R1, LOOP | 7 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 1
Time (until complete) | Name | Busy | Op | Vj | Vk | Qj | Qk
 | Add1 |  |  |  |  |  | 
 | Add2 |  |  |  |  |  | 
14 | Mult1 | Yes | DIVD | 0+R1 | F6 |  | 
 | Mult2 | Yes | DIVD |  |  | #3 | #2
 | Mult3 |  |  |  |  |  | 
 | Mult4 |  |  |  |  |  | 
Reservation Stations
Register Result Status
Reg | F0 | F2 | F6 | R1
ROB # |  | #2 | #4 | 
CDB | ROB #
LD/SD Buffers
Time (until complete) | Name | Busy | Addr | Qj
 | Ld1 |  |  | 
0 | Ld2 | Yes | 8+R1 | 
 | Sd1 | Yes | 16+R1 | #4
 | Sd2 |  |  | 
ROB Entry # | IS | EX | WB | CMT
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
12 |  |  |  | 
13 |  |  |  | 
14 |  |  |  | 
Reorder Buffer /
Instruction Status Iter 2

## Slide 7: Reservation Station Notes

## Slide 10: Tips: How to Update each Slide
Renumber Cycle on Slide
To Issue an Instruction
  Add cycle number when issued
  Update Reservation Station
    Check if instruction inputs are ready (Vi, Vk) or not ready (Qi, Qk)
      If data is not ready, identify which Function Unit will produce using Register Result Status
  For non SD / BR instructions – must update Register Result Status
  Move Tail
To Update Instructions in Execution
  Change time to finish execution
  If time = 0, write in cycle on exe in Instruction Status table
To Update Instructions in Write Result
  For non SD / BR instructions – write FU to CDB
  Fill in cycle number for write back
  Only 1 instruction may write to CDB at a time (but SD / BR can also be in Write Result stage since not using CDB)
  Remove data from reservation station
  Update all Reservation Stations which depended on FU for data
To Commit an Instruction
  Instruction must have finished write back
  Move Head